## Slide 1: HP ProLiant ML110 G5 Server
1. What is new The HP ProLiant ML110 G5 (ML110 G5) is an Intel-based, single processor, entry-level, 4U form factor tower server . It is ideal for single-application IT infrastructure, web, and edge-of-network applications. On 12 November 2007, HP will announce the ML310 G5 as follows: Processor refresh — Quad-Core Intel® Xeon® 3200 processor sequence Options — iLO2 functionality over shared system NIC in support of remote management 2. At-a-glance Available processors — Intel single, dual-core, or quad-core processors: Quad-Core Intel® Xeon® 3200 processor sequence, or Dual-Core Intel® Xeon® 3000 processor sequence, or Dual-Core Intel® Core™2 E4400 processor, or Dual-Core Intel® Pentium® E2160 processor, or Single-Core Intel® Celeron® 420 processor Processor capacity — 1P Form factor — 5U, tower-optimized Memory — Up to 8GB PC2-6400 unbuffered DDR2 ECC 800MHz I/O — Up to 5 Total: (1) PCI Express x8, (3) PCI Express x1, Optional Extender Board for (1) 64-bit/100MHz PCI-X Storage type — Non-hot plug Serial ATA and non-hot plug SCSI Storage controllers — SAS — HP SC40Ge SAS HBA with RAID 0,1 in a PCI Express slot; SATA —Embedded SATA with integrated SATA RAID 0,1 Remote management — Lights Out 100c Remote Management Card High availability — Redundant, hot plug power supply Warranty — Hardware diagnostic support and repair is available for one year from date of purchase. Support for software and initial setup is available for 90 days from date of purchase. SATA hard drives have a one year warranty | 3. Customer opportunities The ML110 G5 is best value and well-suited for: Dependable, easy-to-use workgroup server for hosting basic file/print for 20 or fewer clients Platform for light application hosting, shared web access, groupware, or small database applications Entry-level for small businesses Same price as misapplied desktop PCs Look for customers with the following business requirements: Utilizing one-way ProLiant servers for general purpose or entry-level systems. Why? The ML110 G5 is designed with a balanced architecture to drive the adoption of quad-core technology to its line of single processor systems. The ML110 G5 targets customers with single-tier, simple architectures, homogeneous environments with single applications and workloads, and requires very little IT support. Has a limited budget for server hardware, but Supporting locations with a limited IT staff. Why? The ML110 G5 is well-purposed for small businesses or remote sites with minimal technology skills, limited, or no IT staff. These customers need a reliable server that requires little attention or maintenance and has the warranties and support of a branded-top tier vendor. The ML110 G5 can be remotely managed for remote sites or second offices. Obtaining data protection at an affordable price. Why? This an efficiently sized server that is ideal for small offices, first networks and remote sites. It delivers true server reliability and functionality for the price of a typical desktop computer. | Relying on the server to run industry-standard applications. Why? Ideal applications include file and print, web messaging, small vertical applications or databases, and shared Internet access and LAN infrastructure. Ideal ML110 G5 rely on servers to run day-to-day applications for their growing businesses and they require a server powerful enough to drive these applications. Purchasing an easy-to-own server. Why? Designed specifically for businesses that require an easy-to-configure, easy-to-use platform. All major components are designed to be removed or installed with little effort. When growth becomes necessary for a small business network, the ML110 G5 is easily reconfigurable. 4. Qualifying the customer Green light deals (must win) The customer: Requires enterprise class performance and features Requires remote management capability Requires consistent, reliable server performance at an affordable price Yellow light deals (more qualification) The customer: Is a growing small business with a very limited budget for hardware but requires high availability to meet the needs of their clients Wants to ensure their hardware purchase has a long lifecycle to protect their investment Red light deals (walk away) The customer: Is manually performing back-ups and does not feel their business or infrastructure is adversely impacted by their process 5. Further information/resources For QuickSpecs, white papers, and technical documentation, go to ML110 G5 on HP.com http://www.hp.com/servers/proliantml110
© 2007 Hewlett-Packard Development Company, L.P.
The information contained herein is subject to change without notice.
Quick reference card: HP and channel partner use only

## Slide 2: HP ProLiant ML310 G5 Server
© 2007 Hewlett-Packard Development Company, L.P.
The information contained herein is subject to change without notice.
Quick reference card: HP and channel partner use only
 | HP ProLiant ML310 G5 | Dell PowerEdge 840 | IBM System x3200
Platform | LINUX, Windows | LINUX, Windows | LINUX, Windows
Operating system | Red Hat Linux, SCO UNIX, SUSE Linux, NetWare, Windows | Red Hat Linux, SUSE Linux, Windows | Red Hat Linux, SUSE Linux, Windows
Processor family | Celeron, Core, Pentium, Xeon | Celeron, Pentium, Xeon | Pentium, Xeon
Processor options | Celeron 420 (1.6GHz 35W), Pentium E2160 (1.8GHz 65W), Core 2 Duo E4400 (2.0GHz 65W), Xeon X3065 (2.33GHz 65W), Xeon X3075 (2.66GHz 65W), Xeon X3210 (2.13GHz 95W), Xeon X3220 (2.4GHz 95W) | Celeron 430 (1.8GHz), Pentium D 935 (3.2GHz), Pentium E2160 (1.8GHz) Core 2 Duo (2.2GHz), Xeon 3040 (1.86GHz), Xeon 3050 (2.13GHz) Xeon 3060 (2.4GHz), Xeon 3070 (2.66GHz), Xeon X3210 (2.13GHz) Xeon X3220 (2.4GHz), Xeon X3230 (2.66GHz) | Pentium D 945 (3.4GHz), Pentium E2160 (1.8GHz) Xeon 3040 (1.87GHz), Xeon 3050 (2.13GHz), Xeon 3060 (2.4GHz), Xeon X3210 (2.13GHz), Xeon X3220 (2.4GHz)
Cache | 512KB (Celeron), 1 x 1MB (Pen 2100), 1 x 2MB (Core 2 4000), 1 x 4MB (Xeon 3000) or 1 x 8MB (Xeon 3200) L2 | 512KB L2 (Celeron), 2 x 2MB L2 (Pen D), 2MB (Core 2), 2MB or 4MB L2 (3000 Series) or 2 x 4MB L2 (X3200 Series) | Pentium D: 2 x 2MB L2; Pentium E: 1MB L2; Xeon 3000: 2MB, 4MB L2; Xeon 3200: 8MB
Chipset | Intel 3210 | Intel 3000 | Intel 3010
Memory | 512MB minimum, 8GB maximum, DDR2 SDRAM, unbuffered ECC | 512MB minimum, 8GB maximum, DDR2 SDRAM, unbuffered ECC | 512MB minimum, 8GB maximum, DDR2 SDRAM, unbuffered ECC
Disk controller | 8-port SAS (SAS models), embedded SATA (SATA/SAS models) | SATA | SATA, SAS
Disk maximum internal | 3,000GB | 4,000GB | 3,000GB (SATA only)
RAID support | RAID 0, 1; Optional RAID 1+0, 5, 6 | Optional RAID 0, 1, 5 | Hot Swap: RAID 0,1
Hot swap disks | SAS and SATA | SAS and SATA | SAS and SATA
I/O slot types | 1 x PCI Express x8, x PCI Express x1, 1 x 64-bit, 100MHz PCI-X on optional extender board | 1 x PCI Express x8, 1 x PCI Express x1 2 x PCI-X 64-bit/133MHz, 1 x PCI 32-bit/33MHz | 3 x PCI 32-bit/33MHz, 2 x PCI-Express (one x1 and one x8)
Hot swap/ redundant power supply | Optional | No/No | Standard
Regional contacts | US: Andy Bauman, Andy.bauman@hp.com — Houston, TX USA EMEA: Yan Fei Yang, Yan-fei.yang@hp.com — Meyrin, Switzerland Asia Pacific: Kwang Leng Seah, Kwang-leng.seah@hp.com — Singapore Japan: Seah Sae Iso, Seah-sae.iso@hp.com — Tokyo, Japan |  | 
Source: Competitive Profiles:
http://as.ideascp.com/cp/