## Slide 1
Tru64 Unix Configurations on FC-SW

## Slide 2
Tru64 Unix Configuration FC-Switch
Single Server / Single Controller
HSG80 FC Single Controller
Up to 8 LUNs
Up to 72 Disks
Up to 500 meters per segment
500m
Tru64 Server
Switch
Active
P1
Standby
Single Controller,
One Active Port
Transparent Failover
500m
P2

## Slide 3
Single Server / Single Controller / Dual Port
HSG80 FC Single Controller
Up to 16 LUNs
Up to 72 Disks
Up to 500 meters per segment
500m
P2
Tru64 Server
Switch
Active
P1
Single Controller
Dual Active Port
No Failover
500m
Active
Tru64 Unix Configuration FC-Switch

## Slide 4
Single Server / Dual Controllers
HSG80 FC Dual Controllers
Up to 16 LUNs
Up to 72 Disks
Up to 500 meters per segment
500m
P2
Tru64 Server
Switch
Active
P1
Standby
Dual Redundant
Controllers,
Transparent Failover
Standby
Active
P1
P2
500m
Tru64 Unix Configuration FC-Switch

## Slide 5
Tru64 Unix Configuration FC-Switch
Multiple Servers / Dual Controllers
HSG80 FC Dual Controllers
Up to 16 LUNs/Server
Up to 8 Servers/Switch
Up to 72 Disks
Up to 500 meters per
segment
500m
P2
Tru64 Server
Switch
Active
P1
Standby
Dual Redundant
Controllers,
Transparent Failover
500m
Standby
Active
P1
P2
Tru64 Server
Tru64 Server
Tru64 Server

## Slide 6
Tru64 Unix Configuration FC-Switch
Dual Servers / Dual Controllers / TruCluster
HSG80 FC Dual Controllers
Up to 16 LUNs/Server
Up to 72 Disks
Up to 500 meters per segment
500m
P2
Tru64 Server
Switch
Active
P1
Standby
Dual Redundant
Controllers
Transparent Failover
500m
Standby
Active
P1
P2
Tru64 Server
Switch
NIC or Memory Channel Connection